The bus tracking system uses a quad core processor which is in the Raspberry pi 3 with a GPS module. We use python3 language to program the GPS module to collect the location coordinates. The GPS module uses a USB connection to connect to the Raspberry pi and send data to the Raspberry pi. A python code is written to get the latitude and longitude data from the module and upload the data to ThingSpeak cloud server. The code is listed in listing NUMBER.

Configure GPS module in the Raspberry pi:

To configure the GPS module, connect the module using the USB port in the Raspberry pi USB port.
Now, you have to check the port at which the module is connected.
Go to the terminal and find the following directory
 /dev/tty* ------ //ADD command box around this
To find the serial port ID for the GPS module
ls //IN CMD BOX
then look for tty* files. Do this once with the GPS module connected and once without the module connected to the Raspberry pi and compare the files and find the serial port ID in which the GPS data is being sent. Our serial port ID was ttyACM0 at which the GPS sent its coordinates data.
After you find the serial port, use the following commands to reset and start the GPS module.
*Use this command to list all connected devices viaUSB
lsusb	---- //ADD COMMAND BOX
*Install the gpsd package in your Raspberry Pi
sudo apt-get install gpsd gpsd-clients python-gps	---- //ADD COMMAND BOX
*This will reset the GPS module to collect accurate data from the satellite
sudo systemctl stop gpsd.socket	----------- //ADD COMMAND BOX
sudo systemmctl disable gpsd.socket	-------// ADD COMMAND BOX
After this step you must edit the default gateway by going to the following file and editing the gateway to 0.0.0.0.
emacs /lib/systemd/system/gpsd.socket ---------//ADD COMMAND BOX
*Kills all gpsd processes
sudo killall gpsd ------ //ADD COMMAND BOX
*This sets the path to your GPS module. Add your serial port ID here
sudo gpsd /dev/ttyACM0 -F /var/run/gpsd.sock -------// ADD COMMAND BOX

*To display the GPS values, use this command
gpsmon	-------- // ADD COMMAND BOX
or
cat /dev/ttyACM0 -------- // ADD COMMAND BOX

After the GPS is setup and data is displayed, it needs to be uploaded to the cloud to be read by google maps API.
ThingSpeak:
ThingSpeak cloud server allows us to make fields for uploading different types of data in a graphical representation. We use MQTT API to communicate to the cloud. ThingSpeak has a write API key and a read API key. These keys allow us to write or read the data into the cloud. Code listing will be more elaborative as it is written in python programming language in listing NUMBER.
Thingspeak creates a channel ID and each channel has API keys to communicate with another machine. We use write API key generated by ThingSpeak to upload the location data on ThingSpeak.

We use the following python code to upload our live coordinates to ThingSpeak cloud server.

LISTINGG NUMBER!!!!!
//ADD LISTING
from __future__ import print_function
import serial
import pynmea2
import paho.mqtt.publish as publish
import string
import time

#assigns the serial port to ttyACM0 with 9600 baud rate and a timeout of 0.5 seconds
serialStream = serial.Serial("/dev/ttyACM0", 9600, timeout=0.5)
while(1):
    channelID = "896656"	#Thingspeak channel ID
    writeAPIKey = "HOC815LAIRP0DA2H"	#Thingspeak write API key
    mqttHost = "mqtt.thingspeak.com"	#Thingspeak hostname
    mqttUsername = "Bus tracking data"
    mqttAPIKey = "CCBI1R47UJINGC0O"	#MQTT API key
    tTransport = "websockets"
    tPort = 80
    topic = "channels/" + channelID + "/publish/" + writeAPIKey
    sentence = serialStream.readline().decode()	#reads the GPS data
    if sentence.find('GGA') > 0:
#Converts the data to nmea standards
        data = pynmea2.parse(sentence)
#Uploads the data to the fields created on ThingSpeak
        payload = "field1=" + str(data.latitude) + "&field2=" + str(data.longitude)
#Publish/write the data to the Thingspeak cloud server
        publish.single(topic, payload, hostname=mqttHost, transport=tTransport, po\
rt=tPort,auth={'username':mqttUsername,'password':mqttAPIKey})
        print ("Latitude = ", data.latitude,"Longitude = ", data.longitude)
#Sleeps for 15 seconds as Thingspeak free license allows an update every 15s
        time.sleep(15)

The data get stored in two fields on ThingSpeak called the latitude and the longitude where its displayed in a graphical form. The following image has the Channel stats showing both the fields.

Now, the Location data has to be displayed on google maps. For doing this, we use the Google maps API. An HTML code helps us get the data from ThingSpeak cloud using the read API key and point the location co-ordinates on google maps on a html webpage.
This is how the pointer will point to the bus location on google maps on a webpage.

The html code is shown in listing below to show how the data is collected and displayed on a webpage using google API key. Google API key can be generated and can be used for free.

//ADD LISTING

<html>
 <head>
   <title>UL</title>
   <meta name="viewport" content="initial-scale=1.0, user-scalable=no">
   <meta charset="utf-8">
   <style>

     /* Map height to define the size of the div
       * element that contains the map. */

      #map {
        height: 100%; }
        html, body {
        height: 100%;
        margin: 0;
        padding: 0; }
    </style>
    <script src="https://maps.googleapis.com/maps/api/js?key=AIzaSyDLVP3OxpFJwl9jDfS2ZkNCiuLTic-cXzg"></script>
    <script src="https://ajax.googleapis.com/ajax/libs/jquery/3.1.1/jquery.min.js"></script>
    <script>
      var map;
        var x;
        function loadmaps(){ $.getJSON("https://api.thingspeak.com/channels/896656/fields/1/last.json?api_key=NIA24KP25AC19HO5", function(result){
        var m = result;
        x=Number(m.field1);
        //alert(x); });
$.getJSON("https://api.thingspeak.com/channels/896656/fields/2/last.json?api_key=NIA24KP25AC19HO5", function(result){
        var m = result;
        y=Number(m.field2);
        }).done(function() {
        initialize(); }); }
        window.setInterval(function(){
        loadmaps();
        }, 9000);
      function initialize() {
        //alert(y);
        var mapOptions = {
        zoom: 18,
        center: {lat: x, lng: y} };
        map = new google.maps.Map(document.getElementById('map'),
        mapOptions);
        var marker = new google.maps.Marker({
        position: {lat: x, lng: y},
        map: map });
        var infowindow = new google.maps.InfoWindow({
        content: '<p>Marker Location:' + marker.getPosition() + '</p>'});
        google.maps.event.addListener(marker, 'click', function() {
        infowindow.open(map, marker); }); }
      google.maps.event.addDomListener(window, 'load', initialize);
    </script>
  </head>
  <body>
    <div id="map"></div>
  </body>
</html>